Remote Sensing
Solving the Range Problem
Feb 25, 2025 David Powell

---
The Problem:
The street is at the bottom of the photo. My driveway comes off the street and winds back and forth up the side of the hill to the house (out of the picture at the top right). The brown line going up the hill is my new water line.

---
The Problem: (pg. 4)
- Delivery drivers don’t like coming up my driveway
- I need a way to get packages delivered
- I need to know when a package was delivered, and if it was removed
- It’s too far to run a wire or use WiFi. No cellular service either!

---
What I need is:
- A delivery box where delivery drivers can put my packages
- A way to detect when a package is delivered or removed
- A way to communicate that information to Home Assistant
- A power source that doesn’t need any attention to keep working

---
The Delivery Box
The location of the delivery box, as seen from below the pump house.

---
The Delivery Box
The delivery box hides behind some trees at the bottom of the driveway.

---
Available on Amazon

---
Laser Ranging Module
- VCC – 2.6v to 5.5v
- GND – Ground
- SCL – IIC Clock
- SDA – IIC Data
- GPIO1 – A general purpose mystery output
- XSHUT – Drive this low to hold the device reset (low power)

---
Laser is Infrared (940 nm)

---
ESP D1 Mini

---
0.91” OLED Display

---
RYLR998 LoRa Transciever
- FCC certified
- Built-in antenna
- Reports of reliable 1.5 km range
- Simple AT command structure
- Adjustable power, frequency, baud rate, spreading factor, bandwidth, address, network ID
- Communications can be password protected
- No message delivery confirmation!

---
Battery Manager
Prevents battery over-charge and over-discharge
Can be connected to USB power if needed
4.35-6 volt input
4.2 volt output
Up to 3A discharge capacity
Up to 1A charge capacity

---
Block Diagram
Pump House
Raspberry
Pi
Home
Assistant
House
Delivery Box
Receiver
Transmitter
Package
Fiber Cable

---
Schematic - Sensor/Transmitter

---
Schematic - Receiver

---
Software - Sensor/Transmitter
- Sleeps most of the time; wakes every 5 minutes to check for a package
- All parameters are configurable via the USB serial port
- Display can be disabled to save more power
- Each measurement is an average of 5 readings
- Only reports a change after two consecutive measurements
- A range of measurements can be set for package presence. If measurement is within the range then a package is present.

---
Software - Receiver
- Does not sleep since it is USB powered.
- Listens for incoming JSON-encoded LoRa messages.
- Parses the message and sends an MQTT topic for each element.
- Configuration can be done via USB or MQTT commands.
- MQTT communication is done via WiFi.

---
Hardware Sources
- 3 pcs VL53L0X Laser Distance Module ($6.99)
  https://www.amazon.com/dp/B0CQ28Q3KC
- RYLR998 868/915 MHz Lora Module ($12.60)
  https://www.amazon.com/dp/B099RM1XMG
- 5 pcs ESP8266 Mini D1 Module ($13.99)
  https://www.amazon.com/gp/product/B081PX9YFV
- 2 PCS 0.91'' IIC OLED Display Module ($5.99)
  https://www.amazon.com/gp/product/B07FMDB6TR/
- 3pcs TP4056 18650 Lithium Battery Charger Module
  https://www.amazon.com/dp/B07PKND8KG

---
Resources
- Reyax RYLR998 AT Command User Guide:
  https://manuals.plus/reyax-technology/rylr998-lora-at-command-guide-manual
- VL53L0X Time-Of-Flight Ranging Sensor
  https://www.st.com/resource/en/datasheet/vl53l0x.pdf
- SSD1306 OLED Display Driver Data Sheet
  https://cdn-shop.adafruit.com/datasheets/SSD1306.pdf
- TP4056 Lithium Ion Battery Management Board
  https://dlnmh9ip6v2uc.cloudfront.net/datasheets/Prototyping/TP4056.pdf