## Slide 1: Welcome to H.O.T. www.handsontech.org
Our Purpose:
Forum for interaction
  Many hobbyists build/tinker in isolation
  Make new friends with common tech interests
Learn together
  Lots of fun new tech to explore
  Share expertise, help each other
Build something
  Hands-On learning
  Make something fun & useful

## Slide 2: One Hands-On Tech club Two Groups
3D Printing
Small Computers

## Slide 3: New to the club? Welcome!
Wondering what H.O.T. is all about?
This is a hands-on group, so we may be in the middle of a series of meetings on our way to building something interesting
Go to handsontech.org>New Members for a specially designed launching point for new members!
Please take the time to look through a few presentations at handsontech.org>Small Computers or handsontech.org>3D Printing.
  Presentations are always available online after our meetings for reference and as self-paced projects

## Slide 4: Club communications are via Email & Web !
To join our email list(s), fill membership form at handsontech.org>New Members
  When asked for your email address, use a gmail email address if possible (we use google forums & they are picky)
  You will be added automatically to our Hands-On Tech (H.O.T.) overall email list
  You will also be added to the Small Computers and/or 3D Printing mailing lists and forums if you expressed interest in the membership form.
Meeting calendar is at handsontech.org

## Slide 5
Remote Sensing
Solving Two Problems: Detection and Range
Feb 25, 2025 David Powell

## Slide 6
The Setup:
The street is at the bottom of the photo. The driveway comes off the street and winds back and forth up the side of the hill to the house, which is out of the picture at the top right. The brown line going up the hill is where we installed a new water line recently.

## Slide 7
The Problems:
Delivery drivers don’t like coming up the driveway
Packages need to be delivered safely and securely
The delivery of a package should be announced at the house
It’s too far to run a wire or use WiFi. No cellular service either!

## Slide 8
What is needed:
A delivery box where delivery drivers can put packages
A way to detect when a package is delivered or removed
A way to communicate that information to Home Assistant without cellular or wifi connectivity
A power source that doesn’t require any attention

## Slide 9: The Delivery Box
The delivery box is a plastic deck box that hides behind some trees at the bottom of the driveway.

## Slide 10: Sensing the presence of a package

## Slide 11: HC SR04 Ultrasonic Ranger
These didn’t work in my situation due to ribs in the box.

## Slide 12: I Found These on Amazon

## Slide 13: VL53L0X Operation

## Slide 14
Laser is Infrared (940 nm)

## Slide 15: How to inform Home Assistant when a package is detected or removed?

## Slide 16: RYLR998 LoRa Transciever
FCC certified
Built-in antenna
Reports of reliable 1.5 km range
Simple AT command structure
Adjustable power, frequency, baud rate, spreading factor, bandwidth, address, network ID
Communications can be password protected
Note: No message delivery confirmation!

## Slide 17: Block Diagram
Delivery Box
Pump House*
Receiver
Sensor/Transmitter
Package
WiFi Router
House
Fiber Optic Cable
Home
Assistant
LoRa
* I’m not sure if the LoRa radio will reach all of the way to the house on the dinky built-in antennas. Fortunately, it only has to get to the pump house.

## Slide 18: Pulling it all together

## Slide 19: ESP D1 Mini (x2)

## Slide 20: 0.91” OLED Display (x2)

## Slide 21: A Couple Of Solar Cells, a Battery, and a Charge Controller

## Slide 22: Laser Ranging Module
VCC – 2.6v to 5.5v
GND – Ground
SCL – IIC Clock
SDA – IIC Data
GPIO1 – A general purpose mystery output
XSHUT – Drive this low to hold the device reset (low power)

## Slide 23: Schematic - Sensor/Transmitter

## Slide 24: Sensor Circuit

## Slide 25: Sensor Circuit
Microprocessor Power Supply Supervisor
LDO Regulator

## Slide 26: Software - Sensor/Transmitter
Sleeps most of the time; wakes every X minutes to check for a package (X is TBD)
All parameters are configurable via the USB serial port
Display can be disabled to save even more power
Each measurement is an average of 5 readings
Only reports after two consecutive measurements that indicate a change of status, or an hour has passed
A range of measurements can be set for package presence. If measurement is within the range then a package is present.
Reports with a JSON object via LoRa to the receiver

## Slide 27: Schematic - Receiver

## Slide 28: Software - Receiver
Does not sleep since it is USB powered.
Listens for incoming JSON-encoded LoRa messages.
Parses the message and sends an MQTT topic for each element.
Configuration can be done via USB or MQTT commands.
MQTT communication is done via WiFi.

## Slide 29: Future Enhancements
Better message acknowledgment between LoRa radios
Ability to change configuration parameters of the sensor/transmitter over MQTT
Make the LoRa-to-MQTT receiver more generic, so it may be used with other projects unchanged

## Slide 30: Hardware Sources
3 pcs VL53L0X Laser Distance Module ($6.99) https://www.amazon.com/dp/B0CQ28Q3KC
RYLR998 868/915 MHz Lora Module ($12.60) https://www.amazon.com/dp/B099RM1XMG
5 pcs ESP8266 Mini D1 Module ($13.99) https://www.amazon.com/gp/product/B081PX9YFV
2 PCS 0.91'' IIC OLED Display Module ($5.99) https://www.amazon.com/gp/product/B07FMDB6TR/
3pcs TP4056 18650 Lithium Battery Charger ($5.99) https://www.amazon.com/dp/B07PKND8KG

## Slide 31: Other Resources
Reyax RYLR998 AT Command User Guide: https://manuals.plus/reyax-technology/rylr998-lora-at-command-guide-manual
VL53L0X Time-Of-Flight Ranging Sensor Data Sheet https://www.st.com/resource/en/datasheet/vl53l0x.pdf
SSD1306 OLED Display Driver Data Sheet https://cdn-shop.adafruit.com/datasheets/SSD1306.pdf
TP4056 Lithium Ion Battery Management Board Information https://dlnmh9ip6v2uc.cloudfront.net/datasheets/Prototyping/TP4056.pdf
Complete Project Including STLs, Board Designs, and Code https://github.com/buteomont/Delivery-Box-Reporter-LoRa