Remote Sensing
Solving the Range Problem
Feb 25, 2025 David Powell

---
The Problem:
The street is at the bottom of the photo. My driveway comes off the street and winds back and forth up the side of the hill to the house (out of the picture at the top right). The brown line going up the hill is my new water line.

---
The Problem: (pg. 4)
- Delivery drivers don’t like coming up my driveway
- I needed a way to get packages delivered
- I needed to know when a package was delivered, and if it was removed
- It’s too far to run a wire or use WiFi. No cellular service either!

---
What I needed was:
- A delivery box where delivery drivers could put my packages
- A way to detect when a package was delivered or removed
- A way to communicate that information to Home Assistant
- A power source that doesn’t need any attention to keep working

---
The Delivery Box
The location of the delivery box, as seen from the pump house.

---
The Delivery Box
The delivery box hides behind some trees at the bottom of the driveway.

---
Laser Ranging Module
- VCC – 2.6v to 5.5v
- GND – Ground
- SCL – IIC Clock
- SDA – IIC Data
- GPIO1 – A general purpose mystery output
- XSHUT – Drive this low to hold the device reset (low power)

---
Laser is Infrared (940 nm)

---
Available on Amazon

---
RYLR998 LoRa Transciever
- FCC certified
- Built-in antenna
- Reports of reliable 1.5 km range
- Simple AT command structure
- Adjustable power, frequency, baud rate, spreading factor, bandwidth, address, network ID
- Communications can be password protected
- No message delivery confirmation!

---
ESP D1 Mini

---
0.91” OLED Display

---
Solar Panel and BMS

---
Block Diagram
Pump House
Raspberry
Pi
Home
Assistant
House
Delivery Box
Receiver
Transmitter
Package
Fiber Cable

---
Schematic - Sensor/Transmitter

---
Schematic - Receiver

---
Software - Sensor/Transmitter
- Sleeps most of the time; wakes every 5 minutes to check for a package
- All parameters are configurable via the USB serial port
- Display can be disabled to save more power
- Each measurement is an average of 5 readings
- Only reports a change after two consecutive measurements
- A range of measurements can be set for package presence. If measurement is within the range then a package is present.

---
Software - Receiver
- Does not sleep since it is USB powered.
- Listens for incoming JSON-encoded LoRa messages.
- Parses the message and sends an MQTT topic for each element.
- Configuration can be done via USB or MQTT commands.
- MQTT communication is done via WiFi.

---
Hardware Sources
- 3 pcs VL53L0X Laser Distance Module ($6.99)
  https://www.amazon.com/dp/B0CQ28Q3KC
- RYLR998 868/915 MHz Lora Module ($12.60)
  https://www.amazon.com/dp/B099RM1XMG
- 5 pcs ESP8266 Mini D1 Module ($13.99)
  https://www.amazon.com/gp/product/B081PX9YFV
- 2 PCS 0.91'' IIC OLED Display Module ($5.99)
  https://www.amazon.com/gp/product/B07FMDB6TR/